Order forms

for AUPD automatic booster units

To select optimal automatic booster units according to your requirements you should fill in the order form and send it to us by fax or email.

# A few tips

# Control

Control Type:

Cascade control ensures pressure boosting and maintenance within Pmin to Pmax  range in  water supply systems by switching on/off the necessary amount of pumps in the network mode

Cascade control with soft start/stop protects system from water hammer during start/stop, reduces starting current and increases pump life. We recommend using for drives with more than 4kW power.

Cascade & frequency control changes pump rotation speed, ensure pressure boosting and maintenance in water supply system. Capacity of automated boosting unit is regulated by switching on/off pumps in the network mode depending on water consumption. The first pump is controlled by frequency converter, other pumps are controlled alternately (variable master)

Cascade & frequency control with soft start and stop is recommended to use for drives with more 4 кW power.

Only first pump is controlled by frequency converter (invariable master).

If you need alternative control for all pumps please specify that in Additional requirements.

# Available backup pumps

Amount of available backup pumps is regulated by SNiP (Building Regulations) 2.04.02-85 (Para.7.3).

# Remote monitoring

Remote monitoring through RS-485 protocol MODBUS allows real-time tracking of pump parameters and control them. Max distance is 1,5 km.

# Indication on dispatcher board

Based on electromagnetic relays: operation relay and fault relay

# Backup power supply

Backup power supply is necessary for continuous operation  in case of main power supply failure. Regulated by SNiP (Building Regulations) 2.04.02-85 (Paras. 4.4 and 7.1) and PUE (Rules for Electricity Generating Plants), (Paras. 1.2.17…1.2.20).

# Additional requirements

Here you can specify whether you require hydropneumatic accumulator of necessary volume, temperature control for  - motor winding and pump bearings and any other equipment.

# Customer support:

# Tel. (48677) 7-17-13

# Order form for AUPD automatic booster units

The client	_____________________________________________________________________________________

Scope of activity:	_____________________________________________________________________________________

Contact person	___________________________________________________________________________

Telephone _______________________ fax ______________________ E-mail  _____________________________

Address	________________________________________________________________________________________

| Application | ( Water supply |
| --- | --- |
|  | ( Heating |
|  | ( Other_____________________________________________________ |
| Pumped liquid | ( Tap water |
|  | ( Other liquids ____________________________________________ |
| Liquid temperature | __________ 0С |
| Solids | ( Yes | Concentration __________% | Size __________mm |
|  | ( No |
| suction pressure | Min pressure P1min __________kg/сm2 |
|  | Max pressure P1max __________ kg/сm2 |
|  | Suction head (at water intake from the deepened tank) Hvac __________m |
| discharge pressure | Nom. pressure P2 __________ kg/сm2 |
|  | Min pressure P2min __________ kg/сm2 |
|  | Max pressure P2max __________ kg/сm2 |
| Capacity | Nom. Qnom __________m3/h |
|  | Min Qmin __________m3/h |
|  | Max Qmax __________m3/h |
| Control type | ( Cascade control |
|  | ( Cascade control with soft start & stop |
|  | ( Cascade-frequency control |
|  | ( Cascade-frequency control with soft start & stop |
| Control parameters | ( By pressure |
|  | ( By pressure differential (P __________ kg/сm2 |
|  | ( By temperature t__________0С |
| Available backup pumps | ( Yes | Quantity__________ pcs. |
|  | ( No |
| Remote monitoring | ( Yes |
|  | ( No |
| Indication on dispatcher board | ( Yes |
|  | ( No |
| Power supply | ( 1~220V 50Hz |
|  | ( 3~380V 50Hz |
| Backup power supply | ( Yes |
|  | ( No |

Additional requirements	___________________________________________________________________

______________________________________________________________________________________________________________________________________________________________________________________________

_______________________________________________________________________________________________

# Date _____________________

Your signature ____________________

Note –only fully completed order form accepted .